## Slide 1: Specialty Workshop
Aerodynamics, Weight, & Friction

## Slide 2: Credit where credit is due
Most of these slides are courtesy of:
Mark Westlake
Saint Thomas Academy
mwestlake@cadets.com
Saint Thomas Academy Experimental Vehicle Team (St. Paul Minnesota)
Facebook: https://www.facebook.com/staEVT
Instagram: https://www.instagram.com/sta_evt/

## Slide 3: Aerodynamics vs. Weight
If I were to choose one thing, what would I focus on?
  Dependent on speed
  Track vs. road race
    “Uphills/Downhills” on turns
    Heavier cars have more rolling resistance and take more energy to accelerate. (Much bigger problem in a road race.)
Reliability while perusing the ideal solar car…
  A note of caution about taking things too far when trying to be as efficient as possible
  Do not reduce weight at the cost of safety

## Slide 4: Aerodynamic Drag
Reducing drag is the least expensive way to improve your solar car.

## Slide 5: Aerodynamic Drag

## Slide 6: Aerodynamic Drag
Drag starts at the back of the vehicle, not the front. Hence the name “drag”.
Choose shapes that release airflow smoothly.
Fairings can be made from many common and light weight materials.

## Slide 7: Aerodynamic Drag

## Slide 8: A quick Comparison of Drag
Upright Bike
Velomobile

## Slide 9: Aerodynamic Drag
This is the enemy number one to a solar car’s efficiency.

## Slide 10: Aerodynamic Drag
When you double your speed, the force on your car is 4 times greater!

## Slide 11: Inexpensive Wheel Fairing
Things you need:
  Foam core board
  Razor Blade
  Hot glue
  Carbon fiber or Fiberglass reinforcement
  Epoxy resin
  Creativity
  Body filler

## Slide 12: Wheel Fairings
Cut foam core board to shape
Score with a razor blade
Bend to shape
Glue

## Slide 13: Adding Reinforcement
One or two layers of Carbon or Fiberglass cloth is enough.
Epoxy resin won’t eat through the foam core.
Squeege excess resin from fabric.

## Slide 14: Adding Reinforcement
Add some carbon fiber squares on the inside at attachment points to strengthen foam core board.
Trim with a common jigsaw to fit.

## Slide 15: Final product

## Slide 16: MTEEA Supermileage Body Parts
Cut foam core board to shape
Score with a razor blade
Bend to shape
Hot Glue

## Slide 17: MTEEA Supermileage Body Parts

## Slide 18: MTEEA Supermileage Body Parts

## Slide 19: MTEEA Supermileage Foam Core Body Example

## Slide 20: Adding Vinyl Decals

## Slide 21: Brainerd International Raceway

## Slide 22: Finishing
Reinforcement is covered with a light-weight body filler and sanded smooth.
Prime and paint
(A good painter can cover a lot of flaws!)

## Slide 23: Weight
Heavier cars have more rolling resistance and take more energy to accelerate. (Much bigger problem in a road race.)
Do not reduce weight at the cost of safety.
Making things too light will force you to find an expert welder because things WILL break.

## Slide 24: Rolling Resistance
Bearings can be opened, cleaned, and filled with a light oil.
Tall, skinny, high pressure tires reduce rolling resistance but sacrifice handling.
Tire Proper pressure
If it rotates: lubricate!
Wheel alignment is critical to reducing rolling resistance.

## Slide 25: Specialty Workshop
Solar Car Challenge