## Slide 1: Specialty Workshop
Going Farther on Less

## Slide 2: Aerodynamics and Friction
Going farther on less: getting the most out of your car.
The four things that you can realistically control:
  Electrical efficiency
      Losses due to electrical resistance
      Losses due to poor gearing
  Weight
  Rolling friction
  Aerodynamic drag

## Slide 3: Saint Thomas Academy Experimental Vehicle Team
Our very first project. Built in 1998 for the Minnesota Supermileage Challenge.

## Slide 4
Recognizing the importance of aerodynamics early in our program.

## Slide 5
Our very first Solar Car for the race from Dallas to Pasadena, CA.

## Slide 6
A young Mark Westlake

## Slide 7: Our first (and last!) solar array.

## Slide 8: Our first (and last!) solar array.

## Slide 9: Addition of a Fourth Wheel

## Slide 10: Texas Motor Speedway

## Slide 11
Reduced Frontal Area and Wheel Shrouds

## Slide 12: Solar Commuter Vehicle

## Slide 13
The start of the body.

## Slide 14
The start of the body.

## Slide 15
The start of the body.

## Slide 16
The start of the body.

## Slide 17: The Fiberglass Mold

## Slide 18: The Fiberglass Mold

## Slide 19: Removable Solar Array

## Slide 20: The Carbon Composite

## Slide 21: Build it for less…..

## Slide 23
Shrink wrap and Foam-core

## Slide 24: Solar Car Challenge Battery Electric Division

## Slide 25
Carbon fiber body

## Slide 26: Solar Charging Station

## Slide 27
My friend Lehman Marks

## Slide 28: National Geographic New York City

## Slide 29
No aerodynamics…..but possibly the most fun.

## Slide 30: Drivers’ World Championship

## Slide 31: Pista di Fiorano, Maranello Itay

## Slide 32: Aerodynamics and Friction
Going farther on less: getting the most out of your car.
The four things that you can realistically control:
  Electrical efficiency
      Losses due to electrical resistance
      Losses due to poor gearing
  Weight
  Rolling friction
  Aerodynamic drag

## Slide 33: Design Criteria
Design your car to be efficient from the beginning!
Solar Power: 10% more power will give you a 4% increase in performance.
Aerodynamics: 10% less drag will give you 3.1% increase in performance
Rolling resistance: 10% less resistance will give you 1.3% increase in performance.
Weight: 10% less weight will give you 0.9% increase in performance

## Slide 34: Electrical Efficiency
Choose the correct gauge wire for the current you expect to draw.
  Most cars use 4 gauge or lower for the drive system in the car.
  Soldered connections are more efficient than crimped connections.
  Connections can be checked with an infrared thermometer.
    Heat = energy loss!

## Slide 35
Bench testing electrical system

## Slide 36: Choose the Correct Gears
Don’t gear a car for 50 mph if you are going to drive it at 25 mph. Be realistic about your cars speed!
Chain drive systems can be very efficient if gears are aligned and lubricated.
Pictured: 48V system, 15 tooth front, 70 tooth rear. Max speed = 36 mph

## Slide 37: Weight
Heavier cars have more rolling resistance and take more energy to accelerate. (Much bigger problem in a road race.)
Do not reduce weight at the cost of safety.
Making things too light will cause things to break.

## Slide 38: Rolling Resistance
Bearings can be opened, cleaned, and filled with a light oil.
Tires with thin “supple” casings roll better than thick casings. (Higher risk of flats)
Fat tires roll better than thin tires. (But weigh more.)
If it rotates: lubricate!
Wheel alignment is critical to reducing rolling resistance.

## Slide 39: Aerodynamic Drag

## Slide 40: Aerodynamic Drag

## Slide 41: Aerodynamic Drag
This is the enemy number one to a solar car’s efficiency.

## Slide 42: Aerodynamic Drag
Reducing drag is the least expensive way to improve your solar car.
The extra weight of drag reducing fairings is easily made up for in aerodynamic efficiency.

## Slide 43: Aerodynamic Drag
Drag starts at the back of the vehicle, not the front. Hence the name “drag”.
Choose shapes that release airflow smoothly.
Fairings can be made from many common and light weight materials.

## Slide 44: Aerodynamic Drag
When you double your speed, the force on your car is 4 times greater!

## Slide 45: Relative Aerodynamic Drag

## Slide 46: Barn Owl

## Slide 47: Ecomodders and HPVers
International Human Powered Vehicle Association https://www.ihpva.org/home/
Automotive Economy Modifications https://ecomodder.com/

## Slide 48
10-15% increase in efficiency.

## Slide 49: Inexpensive Solutions

## Slide 50: Inexpensive Solutions

## Slide 51: Fairings for Tubes
3D Printed in segments

## Slide 52: Energy Savings
For a 1 meter long, 1 inch diameter tube traveling 20 mph:
 | Round Tube | Aerodynamic Tube
Drag Force (Newtons) | 1.5 | 0.18
Energy per Lap (Joules) | 3621 | 434
Power Needed (Watts) | 13.5 | 1.7
Energy for 10 Laps (Joules) | 36,210 (36kJ) | 4340 (4.3kJ)
Energy for 300 Laps (kilojoules) | 1086.3 kJ | 130.2 kJ
Four Tubes | 4345.2 kJ | 520.8 kJ
You use about 1.5% of your solar array just to push tubes through the air! (Approximately 4 solar cells at 20mph, 6 solar cells at 30mph)
It takes more than 8 times the energy to push a round tube through the air than an aerodynamic tube!

## Slide 53: Inexpensive Wheel Fairing
Things you need:
  Foam core board
  Razor Blade
  Hot glue
  Carbon fiber or Fiberglass reinforcement
  Epoxy resin
  Creativity
  Body filler

## Slide 54: Wheel Fairings
Cut foam core board to shape
Score with a razor blade
Bend to shape
Glue

## Slide 55: Adding Reinforcement
One or two layers of Carbon or Fiberglass cloth is enough.
Epoxy resin won’t eat through the foam core.
Squeege excess resin from fabric.

## Slide 56: Adding Reinforcement
Add some carbon fiber squares on the inside at attachment points to strengthen foam core board.
Trim with a common jigsaw to fit.

## Slide 57: Finishing
Reinforcement is covered with a light-weight body filler and sanded smooth.
Prime and paint
(A good painter can cover a lot of flaws!)

## Slide 58: A complete car from foamcore

## Slide 59: A complete car from foamcore

## Slide 60: A complete car from foamcore

## Slide 61: A complete car from foamcore

## Slide 62: Shrink Wrap Body Cover
Made from 7-mil shrink-wrap that is used to protect boats in the winter.
Shrink-wrap is cut to shape and taped to the car with inexpensive tape that is made for the material.
A common heat gun can be used to shrink the material.
The material cools and maintains a semi-rigid surface.
Easily repaired with tape.

## Slide 63: Cut and Tape the Material

## Slide 64: Reinforce and Heat

## Slide 65: Trim to fit around fairings
Shrink Wrap
Big Shrink www.bigshrink.com
Comes in a variety of colors and thicknesses

## Slide 66: Final product

## Slide 67: What is the Saint Thomas Academy Experimental Vehicle Team up to now?

## Slide 68: 3D Printed Mold

## Slide 69: CAD Drawing of Mold Parts

## Slide 70: Mold complete

## Slide 71: Carbon Fiber Composite Parts

## Slide 72: Finished Hydrogen Fuel-cell Vehicle

## Slide 73: Contact information
Mark Westlake
mwestlake@cadets.com
Saint Thomas Academy Experimental Vehicle Team (St. Paul Minnesota)
Facebook: https://www.facebook.com/staEVT
Instagram: https://www.instagram.com/sta_evt/

## Slide 74: Specialty Workshop
Solar Car Challenge